## Slide 1
The Use Of Genetic Algorithms In Airfoil Design And CFD
Definitions
Genetic Algorithm: A type of algorithm that approximates a solution to a complex problem. They act like evolution, where the better the potential solution, the more likely it is to influence the next generation.
CFD: Computation Fluid Dynamics – Using complex computer programs to simulate the flow of fluids around and through a system.
Conclusion
Genetic algorithms are useful to discover if there are any bugs in a solver as they will find and exploit them if there are any.
If the system is properly constrained, like Study 3, then genetic algorithms can produce a near-perfect result.
If left to run for long enough then genetic algorithms will stop producing accurate results as the solver won’t give a higher result.
Scan to see all the code I used to make this ➔
Study 1
In my first test, I started with a population of random points, and combined the individual points, usually with a bit of mutation. It clearly hasn’t worked.
More details ⬆
Study 3
In my third test, I started with NACA 4-digit airfoils, but combined them by averaging the maximum camber deviation, location and thickness of the airfoils.
More details ⬆
Study 2
In my second test, I started with a population of NACA 4-digit airfoils, then combined them in the same way as test 1. This worked a lot better, but there is still a bit of bumpiness because the solver isn’t perfect.
⬆ More details
Study 4
In this test, I recorded the maximum, mean and minimum scores of all airfoils in the population. I did the same test as Study 3, but I plotted how the L/D changed as the generations progressed.
⬆ More details
Starting | Random points
Combining | Averaging points
L/D | Infinity
Starting | Airfoils
Combining | Averaging points
L/D | 494
Starting | Airfoils
Combining | Average parameters
L/D | 
Parameters
Population | 10,000
Mutation rate | 5%
Elites | 50
Generations | 1750
Selection | Top half
Fitness | Lift over drag (L/D)
Aim
To explore the use of genetic algorithms to speed up airfoil design, and how they can help the most. I tested 3 different optimization methods, each altering different factors, and recorded the progress through generations.